011106-final rule submission

INTERNATIONAL FINN CLASS: RULE CHANGE SUBMISSIONS (w/amendts to 06/11).

INTERNATIONAL FINN CLASS

The following amendments to the Class Rules have been approved to be effective 1st March 2002.

Rule 1.5.3	Measurers who are interested parties.

New Rule:

1.5.3	renumber to 1.5.3.1 and add at start:  ”Except as prescribed by Rule 1.5.3.2, a Measurer shall not…”

New Rule:

1.5.3.2	Add new rule:  A person who is an interested party as described by Rule 1.5.3.1 may be approved as in Rule 1.5.1.1 for the measurement of masts, booms, sails or rudders at the manufacturer’s premises.

Rule 4.2.6.3	Mast Bearing Play.

New Rule:

4.2.6.3	The fore-and-aft movement at the masthead due to play at the deck and heel bearing systems, shall not exceed 10 cm, when measured in the prescribed manner. 	With the boat held stern down, a light line shall be rigged at a constant tension from the masthead halyard sheave to the top of the transom.  The mast shall be pushed maximum forward and maximum aft to take up play at the bearings.  The difference in the distance from the masthead to the transom shall not exceed 10 cm.

# Rule 4.6.2.3	Recommended Standards for Mast Bearings and Boom Attachments.

## New Rule:

4.6.2.3	Add at end of existing Rule:

“Standard sizes are recommended for mast bearings and boom attachments.  Masts complying should be marked “C” near the boom attachment.

The diameter of the standard mast bearing at the deck shall be 103 mm ±1mm.

The diameter of the standard mast bearing at the heel shall be 63 mm +1mm.

The standard boom shall be attached by a standard fork fitting on the mast.  The width between arms of the fork shall be minimum 37 mm, maximum 40 mm.  A pin shall be provided, diameter 16 mm ±0.5mm. The holes shall be 16 mm diameter ±0.5mm.  The center of the holes shall be not less than 820 mm above the heel and not more than 40 mm aft of the “Aft Edge Line”.

Rule 4.6.5.1	Mast Labels.

New Rule:

4.6.5.1	Every mast built after 1 March 2001 shall have an IFA Mast Label attached within 1 metre above the deck bearing.

Rule 4.6.5.3	Mast Labels.

New Rule:

4.6.5.3	Plastic Masts built before 1 March 2001 shall have an IFA Mast Label attached within 1 metre above the deck bearing.

Include remark:

4.6.5.3  This may be issued by class officials on production of the completed Mast Measurement Card for the mast.

# Rule 4.7.3.4	Recommended Standards for Boom Attachments to Masts

New Rule:

4.7.3.4	Standard sizes are recommended for boom attachments. Booms complying should be marked “C” near the boom attachment.

The standard boom shall be attached to the mast by a standard fork fitting.  The pin hole shall be 16 mm diameter ± 0.5 mm.  It shall be centred not less than 40 mm below the top of the boom.

In compliance with Rule 4.7.3.2, the distinctively coloured band on the boom shall be not more than 3230 mm from the centre of the boom pin hole, measured along the top of the boom.

# Rule 5.7	Propulsion

New Rule:

5.7.1	In alteration to RRS 42.3 (b):

Except on a beat to windward, when surfing (rapidly accelerating down the leeward side of a wave) or planing is possible, the helmsman may pull the sheet in order to initiate surfing or planing, but not more than three times for each wave or gust of wind.

5.7.2	In alteration to RRS 42:

.1	Flag [2nd.Substitute] displayed at the start or near a mark, indicates that: “After starting or rounding the nearby mark, RRS 42 is varied in that except on a beat to windward, pumping, rocking and ooching are permitted.”

.2	Flag [R] displayed near a mark, indicates that:  “After rounding the nearby mark, RRS 42 is varied only by Class Rule 5.7.1”.

5.7 Remark:

The provisions of 5.7.2.1 are intended for application when stronger wind and wave conditions are present.

### MAST MEASUREMENT CARDS

#### Old Wording:

INTERNATIONAL FINN CLASS MEASUREMENT CARD

MAST

Measurer’s stamp and serial number (placed near the boom hinge) ………………………………………

4.6.1		Materials ………………………………………………………………………………………

4.6.1.1		Material of the sail track ……………………………………………………………………

4.6.2		Construction

4.6.2.1/4.6.2.2 ……………………………………………………………………………………… (complies)

4.6.2.3		Diameter at Deck ………………100 mm <…………………………………………………

4.6.2.4		Width …………………………………………………………………………… (complies)

4.6.2.5		Fore-and-aft …………………………………………………………………… (complies)

4.6.2.6 to 4.6.2.9	…………………………………………………………………………… (complies)

4.6.3.1/4.6.3.2	Measurement Bands …………………………………………………………… (complies)

4.6.4.1		Weight ……………………………………………………………………………… (< 8 kg)

4.6.4.2		Corrector Weight …………………………………………………………………… (< 1 kg)

4.6.4.3 		Height of Centre of Gravity …… 2400< ……………………………………………………

(…2200< …………………………………………… for masts weighing more than 10kg)

### MAST MEASUREMENT CARDS

#### New Wording:

Supplier’s Letterhead with any Logo, Address, Telephone, E-Mail etc.

Suppliers of International Finn Class Masts.. .. etc. (not more than one line)

This is to Certify that the Mast has been built in accordance with the current Rules of the International Finn Class, that the Mast Label has been correctly obtained from the International Finn Association, and that to the best of my knowledge and belief the mast has passed correct measurement from the authorized Measurer below.

Signed (Mast Manufacturer or Representative) ……………………………………………………………

Date	…………………………………… Date of Manufacture ……………………………………………

INTERNATIONAL FINN CLASS MEASUREMENT CARD

MAST

4.6.5.1		IFA Mast Label attached ………………Number……………………………………………………

Date of Measurement) …………………………………………………………………………………

4.6.5.2		Measurer (print and sign) ………………………………………………………………………………

Measurer authorized by: ………………………………………………………………………………

4.6.1		Materials …………………………………………………………………………………………………

4.6.1.1		Material of the sail track ………………………………………………………………………………

4.6.2		Construction

4.6.2.1/4.6.2.2	……………………………………………………………………………………………… (complies)

4.6.2.3		Diameters at Deck and heel ………………………………………………………… (>73, >62 mm)

4.6.2.4		Width ……………………………………………………………………………………… (complies)

4.6.2.5		Fore-and-aft ……………………………………………………………………………… (complies)

4.6.2.6 to 4.6.2.9	……………………………………………………………………………………………… (complies)

4.6.3.1/4.6.3.2	Measurement Bands …………………………………………………………………… (complies)

4.6.4.1		Weight with Correctors ……………………………………………………………………… (> 8 kg)

4.6.4.2		Corrector Weight …………………………………………………………………………… (< 1 kg)

4.6.4.2		Height of Corrector Weight …………………………………………………………………………

4.6.4.3 		Height of Centre of Gravity …………………………………………………………… (>2400 mm)

THIS MAST   DOES / DOES NOT   COMPLY WITH

THE RECOMMENDED STANDARD DIMENSIONS IN RULE 4.6.2.3.

Compliance Mark (C) if applicable……………………………………………Y/N